## Slide 1: CUDA Profiling and Debugging
Shehzan
ArrayFire

## Slide 2: Summary
ArrayFire
GPU Programming and CUDA
Debugging and Profiling using CUDA Tools
Memory Coalescing
Shared Memory and Bank Conflicts
Transpose
Reduction
Notes: A lot of the programming concepts have been covered in theory. Today we will see how to find these places and apply optimizations

## Slide 3: ArrayFire
Awesomely Fast GPU Library
CUDA, OpenCL
Write once. Run anywhere
Going Open Source!
www.accelereyes.com
Notes: Releasing on Sept 30
First OpenCL library

## Slide 4: ArrayFire
High-level GPU Library
Features
  Scalar and vector math
  Matrix ops
  Linear algebra & data analysis
  Image and signal processing
  Graphics
  Integrate with your CUDA/OpenCL code
Windows, Linux and Mac
www.accelereyes.com
Notes: Releasing on Sept 30
First OpenCL library

## Slide 5: ArrayFire
What do I do?
  Currently working on getting open-source ready
  95% time coding
  5% Settlers of Catan
  Go-to guy for Windows
www.accelereyes.com
Notes: Releasing on Sept 30
First OpenCL library

## Slide 6: CUDA
Overview
Notes: Quick overview
Most of it covered by Patrick

## Slide 7: What is CUDA
Compute Unified Device Architecture
The Architecture
  Expose GPU computing for general purpose
CUDA C/C++
  Extensions to the C/C++ language to enable heterogeneous programming
  APIs to manage devices and memory

## Slide 8: Debugging and Profiling
NVIDIA Nsight Visual Studio Edition

## Slide 9: Debugging
Host side
  Visual Studio Debugger, gdb
Device side
  Nsight, cuda-gdb (linux)

## Slide 10: CUDA Tools
Debugging : Nsight / CUDA GDB
Profiling : NV Visual Profiler, Nsight
Runtime : CUDA Occupancy Calculator

## Slide 11: CUDA GDB (Linux)
CUDA-GDB
  An extension of GDB
  Allows you to debug on actual hardware
  Can debug CPU and GPU code
Compile using the -g and the -G flags
  Includes debug info
  nvcc -g -G foo.cu -o foo
Usage of cuda-gdb is similar to gdb
For more information, shoot me an email!

## Slide 12: Debugging Coordinates
Software Coordinates
  Thread
  Block
  Kernel
Hardware Coordinates
  Lane (thread)
  Warp
  SM
  Device
Notes: Lane is a thread executing on a device
Warp is a set of 32 currently active threads

## Slide 13: NVIDIA Nsight VSE

## Slide 14: NVIDIA Nsight VSE
Comprehensive debugging and profiling tool
Contents:
  GPU Debugger
  Graphics Inspector
  System Profiling
More information than you know what to do with
NVIDIA Nsight Visual Studio Documentation
Notes: We will be demoing only debugger today.
Graphics debugging is awesome.

## Slide 15: NVIDIA Nsight VSE
GPU Debugging
  CUDA Debugger
  CUDA Memcheck
  CUDA Profiling
  Trace

## Slide 16: Enable Nsight Debugging
Turn on Debug Info
  Project->Properties->CUDA C/C++->
    Generate GPU Debug Info
    Generate Host Debug Info
Best to run at highest compute available

## Slide 17: NVIDIA Nsight VSE
Demo
Credits:
Vector Add - CUDA Samples
Resize – ArrayFire Source Code
Nsight Fluids GL Tutorial – NVIDIA
  https://developer.nvidia.com/nsight-visual-studio-edition-videos
Notes: Demos to run:
CUDA Samples -> Simple -> Matrix Mul
Show debug info, debug focus, cuda info, warp watch
Profiling application
Generating trace
ogl_samples -> gl-420-texture-cube
Unwrapping texture
Viewing and debugging glsl
Show --line-info parameter

## Slide 18: NVIDIA Visual Profiler

## Slide 19: NVIDIA Visual Profiler
Standalone application with CUDA Toolkit
Visualize performance
Timeline
Power, clock, thermal profiling
Concurrent profiling
NV Tools Extensions API
nvprof - command line tool
http://docs.nvidia.com/cuda/profiler-users-guide/index.html#visual-profiler
Notes: Thermal profiling with CUDA 5.5
Kernels of one cuda version will not execute with NVVP of another version
Concurrent profiling - For dynamic parallelism

## Slide 20: NVIDIA Visual Profiler
Demo
Notes: 800 Contacts comparison - Before and after split
Path tracer - Run 5 or 10 frames
Further use in transpose and reduction

## Slide 21: Memory Coalescing
Super awesome speed up

## Slide 22: Memory Coalescing
Coalesce access to global memory
  Most important performance consideration
  Loads and stores by threads of a warp can be combined into as low as one instruction
The concurrent accesses of the threads of a warp will coalesce into a number of transactions equal to the number of cache lines necessary to service all of the threads
Notes: Threads in a warp are continuous. They execute the same command at the same time.
So why not have them access the same are of the memory. This is memory coalescing and works really fast
Basically says continuous/concurrent memory access is better

## Slide 23: Coalescence
A warp requests 32 aligned, 4-byte words
  32 threads requesting 1 float each (continuous in memory)
Address fall within 1 L1 cache-line
  Warp needs 128 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 100%
...
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
...
L1
L2
Notes: A warp has 32 threads
They execute command to fetch 4-byte words ie. ints or floats in sequential order
[i] = [j]
[i+1] = [j+1]

## Slide 24: Coalescence
A warp requests 32 aligned, 4-byte words
  32 threads requesting 1 float each (continuous in memory)
  Not sequentially indexed
Address fall within 1 L1 cache-line
  Warp needs 128 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 100%
...
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
...
L1
L2
Notes: A warp has 32 threads
They execute command to fetch 4-byte words ie. ints or floats in non-sequential order
[i+y] = [j+x]
However, this does not affect performance negatively since we are not using excess memory space.

## Slide 25: Coalescence
A warp requests 32 aligned, 4-byte words
  32 threads requesting 1 float each (not all continuous in memory)
Address fall within 2 L1 cache-line
  Warp needs 128 bytes
  256 bytes move across the bus on a miss
  Bus utilization: 50%
...
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
...
L1
L2
Notes: A warp has 32 threads
They execute command to fetch 4-byte words ie. ints or floats in sequential order of say alternating elements
This means 256 bytes are fetched although only 128 bytes are accessed.
Why are 256 bytes fecthed? because we are using caches. So continuous data is copied from global to cache and then to threads
[i] = [j]
[i+1] = [j+2]
[i+2] = [j+4]

## Slide 26: Coalescence (Non-cached)
A warp requests 32 aligned, 4-byte words
  32 threads requesting 1 float each (not all continuous in memory)
Address fall within 5 L2 cache-line
  Warp needs 128 bytes
  160 bytes move across the bus on a miss
  Bus utilization: 80%
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
L1
L2
...
Notes: A warp has 32 threads
They execute command to fetch 4-byte words ie. ints or floats in sequential order of say alternating elements
This means 160 bytes are fetched although only 128 bytes are accessed.
Why are 160 bytes fecthed? because we are not using caches. So continuous data is copied from global to cache and then to threads
If we were using cache, then 2 L1 blocks would have been occupied which would need 256 bytes to move across the bus.

## Slide 27: Coalescence
A warp requests 1 4-byte word
  All 32 threads requesting 1 float value
Address falls within 1 L1 cache-line
  Warp needs 4 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 3.125%
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
...
L1
L2
Notes: Even though 1 element is access by all threads, the entire memory block needs to be copied
128 bytes in case of L1 and 32 in case of L2

## Slide 28: Coalescence (Non-cachED)
A warp requests 1 4-byte words
  All 32 threads requesting 1 float value
Address fall within 1 L2 cache-line
  Warp needs 4 bytes
  32 bytes move across the bus on a miss
  Bus utilization: 12.5%
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
L1
L2
Notes: Even though 1 element is access by all threads, the entire memory block needs to be copied
128 bytes in case of L1 and 32 in case of L2

## Slide 29: Coalescence
A warp requests 32 scattered 4-byte words
  Randomly stored in memory
Address fall within N L1 cache-line
  Warp needs 128 bytes
  N * 128 bytes move across the bus on a miss
  Bus utilization: 128 / (N * 128)
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
...
L1
L2
...
Notes: Generalization of cases discussed

## Slide 30: Coalescence (Non-cached)
A warp requests 32 scattered 4-byte words
  Randomly stored in memory
Address fall within N L1 cache-line
  Warp needs 128 bytes
  N * 32 bytes move across the bus on a miss
  Bus utilization: 128 / (N*32)
addresses from a warp
96
192
128
160
224
288
256
32
64
352
320
384
448
416
Memory addresses
0
L1
L2
...

## Slide 31: Shared Memory

## Slide 32: Shared Memory
Acts as a user-controlled cache
Declared using the __shared__ qualifier
Accessible from all threads in the block
Lifetime of the block
Allocate statically or at kernel launch.
__shared__ float myVariable[32];
// ... or specify at launch:
extern __shared__ float myVar[];
myKernel<<<blocks, threads, shared_bytes>>>(parameters);

## Slide 33: Shared Memory
Inter-thread communication within a block
Cache data to reduce redundant global memory access
Improve global memory access patterns
Divided into 32 32-bit banks
  Can be accessed simultaneously
  Requests to the same bank are serialized
Notes: Total shared memory per block depends on GPU, but most have 48K

## Slide 34: Shared Memory
Will revisit….
Notes: Total shared memory per block depends on GPU, but most have 48K

## Slide 35: Matrix Transpose
Get 90% Bandwidth
Notes: Take a paper and write down how much of a speed up you can get over CPU

## Slide 36: Matrix Transpose
Inherently parallel
  Each element independent of another
Simple to implement
1 | 2 | 3 | 4
5 | 6 | 7 | 8
9 | 10 | 11 | 12
13 | 14 | 15 | 16
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15
4 | 8 | 12 | 16

## Slide 37: Matrix Transpose [CPU Transpose]
for(int i = 0; i < rows; i++)
for(int j = 0; j < cols; j++)
transpose[i][j] = matrix[j][i]
Easy
O(n2)
Slow!!!!!!

## Slide 38: Matrix Transpose [Naive GPU Transpose]
GPU Transpose
  Launch 1 thread per element
  Compute index
  Compute transposed index
  Copy data to transpose matrix
O(1) using Parallel compute
Essentially one memcpy from global-to-global
  It should be fast, shouldn’t it?

## Slide 39: Matrix Transpose [Naive GPU Transpose]
__global__
void matrixTranspose(float *_a, float *_b) {
int i = blockIdx.y * blockDim.y + threadIdx.y; // row
int j = blockIdx.x * blockDim.x + threadIdx.x; // col
int index_in = i*cols+j; // (i, j) from matrix A
int index_out = j*rows+i; // transposed index
b[index_out] = a[index_in];
}
2 | 5 | -2 | 6 | 6
3 | 5 | 3 | 4 | 6
4 | 8 | 4 | -1 | 3
2 | 3 | 4
5 | 5 | 8
-2 | 3 | 4
6 | 4 | -1
6 | 6 | 3
_a[ . . . . . .]
_b[ . . . . . .]

## Slide 40: Matrix Transpose [Naive GPU Transpose]
Problems?

## Slide 41: GMEM Access Pattern in NT
2 | 3 | 4 | 5 | 5 | 8 | -2 | 3 | 4 | 6 | 4 | -1 | 6 | 6 | 3
2 | 5 | -2 | 6 | 6 | 3 | 5 | 3 | 4 | 6 | 4 | 8 | 4 | -1 | 3
_a
_b
READ - Coalesced memory access
WRITE - Uncoalesced memory access
Good!
Bad!
Notes: Kept this diagram from using earlier
Each element also represents a thread

## Slide 42: Matrix Transpose [Naive GPU Transpose]
Problems?
  Non-coalesced memory
Improvements?

## Slide 43: Matrix Transpose [Naive GPU Transpose]
Problems?
  Non-coalesced memory
Improvements?
  Use shared memory
  Use coalesced memory access

## Slide 44: Matrix Transpose [GPU Transpose]
Use Shared Memory
  Allows temporary storage of data
  Use coalesced memory access to global memory
Walkthrough
  Compute input index (same as in naive transpose)
  Copy data to shared memory
  Compute output index
    Remember, coalesced memory access
    Hint, transpose only in shared memory
  Copy data from shared memory to output
Notes: Lets flip it in shared memory
Use __syncthreads

## Slide 45: Memory Access Pattern for SMT
2 | 3 | 4 | 5
8 | 3 | 5 | 3
1 | 0 | 5 | 9
1 | 9 | 8 | 4
…
…
…
2 | 3 | 4 | 5
8 | 3 | 5 | 3
1 | 0 | 5 | 9
1 | 9 | 8 | 4
2 | 8 | 1 | 1
3 | 3 | 0 | 9
4 | 5 | 5 | 8
5 | 3 | 9 | 4
…
…
…
2 | 8 | 1 | 1
3 | 3 | 0 | 9
4 | 5 | 5 | 8
5 | 3 | 9 | 4
__syncthreads();
re-indexing
SHARED
MEMORY

## Slide 46: Shared Memory Transpose

## Slide 47: Transpose: Shared Memory
__global__
void matrixTransposeShared(const float *_a, float *_b){ __shared__ float mat[BLOCK_SIZE_X][BLOCK_SIZE_Y];
int bx = blockIdx.x * BLOCK_SIZE_X;
int by = blockIdx.y * BLOCK_SIZE_Y;
int i = by + threadIdx.y; int j = bx + threadIdx.x; //input
int ti = bx + threadIdx.y; int tj = by + threadIdx.x; //output
if(i < rows && j < cols)
mat[threadIdx.x][threadIdx.y] = a[i * cols + j];
__syncthreads(); //Wait for all data to be copied
if(tj < cols && ti < rows)
b[ti * rows + tj] = mat[threadIdx.y][threadIdx.x];
}

## Slide 48: Matrix Transpose [GPU Transpose]
Problem?

## Slide 49: Matrix Transpose [GPU Transpose]
Problem?
  Why are we not even close to max bandwidth?
  Hint, think “banks”
Solution?

## Slide 50: Matrix Transpose [GPU Transpose]
Problem?
  Why are we not even close to max bandwidth?
  Hint, think “banks”
Solution?
  Remove bank conflicts

## Slide 51: Bank Conflicts

## Slide 52: Banks
Shared Memory is organized into 32 banks
Consecutive shared memory locations fall on different banks
Bank 1
Bank 2
Bank 3
Bank 31
Bank 30
Bank 4
Bank 5
...
...
Warp
0
1
2
3
4
30
31
32
33
34
35
36
62
63
__shared__ float tile[64];

## Slide 53: Banks
Access to different banks by
a warp executes in parallel.
Bank 1
Bank 2
Bank 3
Bank 31
Bank 30
Bank 4
Bank 5
...
...
Warp
0
1
2
3
4
30
31
32
33
34
35
36
62
63
__shared__ float tile[64];
int tidx = threadidx.x;
float foo = tile[tidx] - 3;

## Slide 54: Banks
Access to the same element
in a bank is also executed
in parallel.
Bank 1
Bank 2
Bank 3
Bank 31
Bank 30
Bank 4
Bank 5
...
...
Warp
0
1
2
3
4
30
31
32
33
34
35
36
62
63
__shared__ float tile[64];
int tidx = threadidx.x;
int bar = tile[tidx - tidx % 2];

## Slide 55: Banks
Access to the different elements in a bank is executed serially.
“2 way bank conflict”
Bank 1
Bank 2
Bank 3
Bank 31
Bank 30
Bank 4
Bank 5
...
...
Warp
0
1
2
3
4
30
31
32
33
34
35
36
62
63
__shared__ float tile[64];
int tidx = threadidx.x;
tmp = tile[tidx + tidx % 2*31];
Notes: Threads want alternate elements which means 2 threads want elements from the same bank

## Slide 56: Banks
Access to the different elements in a bank is also executed serially.
32 way bank conflict
Bank 1
Bank 2
Bank 3
Bank 31
Bank 30
Bank 4
Bank 5
...
...
Warp
0
1
2
3
4
30
31
32
33
34
35
36
62
63
_b[index_out] = tile[tx][ty];
Notes: All threads want memory from the same bank

## Slide 57: Transpose: Shared Memory
__global__
void matrixTransposeShared(const float *_a, float *_b) {
__shared__ float mat[BLOCK_SIZE_X][BLOCK_SIZE_Y];
int bx = blockIdx.x * BLOCK_SIZE_X;
int by = blockIdx.y * BLOCK_SIZE_Y;
int i = by + threadIdx.y;
int j = bx + threadIdx.x; //input
int ti = bx + threadIdx.y;
int tj = by + threadIdx.x; //output
if(i < rows && j < cols)
mat[threadIdx.x][threadIdx.y] = a[i * cols + j];
__syncthreads(); //Wait for all data to be copied
if(tj < cols && ti < rows)
b[ti * rows + tj] = mat[threadIdx.y][threadIdx.x];
}
Represents row of the “bank”
Represents bank number or “col”
Same for all threads in the warp
Notes: If we look at this code, we notice that threadIdx.x is used as the second index.
We can safely assume that for all threads in the warp, threadIdx.y will be same (because of block size)
Hence, threadIdx.y, which represents the same bank in shared memory, is same for all threads in the warp.
Hence a 32-way bank conflict.

## Slide 58: Shared Memory Transpose

## Slide 59: Transpose
No Bank conflicts
Thread 0
Thread 31
Add Unused column

## Slide 60: Transpose
32-way Bank conflict!!
Thread 0
Thread 31
Add Unused column

## Slide 61: Banks
Resolving bank conflict
Elements per row = 32
Shared Mem per row = 33
1 empty element per memory row
  This is what avoid bank conflicts
  Tile[0][0] = 0 = 0 -> Bank 0
  Tile[1][0] = 0 + 33 = 33 -> Bank 1
  Tile[2][0] = 0 + 33 + 33 = 66-> Bank 2
  Tile[n][0] = 0 + n * 33 -> Bank n
Bank 1
Bank 2
Bank 3
Bank 31
Bank 30
Bank 4
Bank 5
...
...
Warp
0
1
2
3
4
30
31
32
33
34
35
36
62
63
__shared__ float tile[BLOCKSIZE][BLOCKSIZE+1];
_b[index_out] = tile[tx][ty];

## Slide 62: Transpose: Shared Memory No Bank Conflicts
__global__
void matrixTransposeShared(const float *_a, float *_b) {
__shared__ float mat[BLOCK_SIZE_X][BLOCK_SIZE_Y + 1];
//Rest is same as shared memory version
}

## Slide 63: Matrix Transpose [GPU Transpose]
Very very close to production ready!
More ways to improve?
  More work per thread - Do more than one element
  Loop unrolling

## Slide 64: Transpose: Loop Unrolled
More work per thread:
  Threads should be kept light
  But they should also be saturated
  Give them more operations
Loop unrolling
  Allocate operation in a way that loops can be unrolled by the compiler for faster execution
  Warp scheduling
    Kernels can execute 2 instructions simultaneously as long as they are independent

## Slide 65: Transpose: Loop Unrolled
Use same number of blocks, shared memory
Reduce threads per block by factor (side)
Block Size X = 4
Block Size Y = 4
Threads/Block = 16
Total blocks = 2
Shared mem = 4 x 4
Block Size X = 4 -> TILE
Block Size Y = 1 -> SIDE
Threads/Block = 4
Total blocks = 2
Shared mem = TILE x TILE
Notes: Using same number of blocks but using less threads per block.
This means less warps to execute
Note: not all GPUs may see a performance benefit

## Slide 66: Transpose: Loop Unrolled
Walkthrough
Host:
  Same number of blocks
  Compute new threads per block
Device:
  Allocate same shared memory
  Compute input indices similar to before
  Copy data to shared memory using loop (k)
    Unrolled index: add k to y
  Compute output indices similar to before
  Copy data from shared memory into global memory
    Unrolled index: add k to y

## Slide 67: Transpose: Loop Unrolled
const int TILE = 32; const int SIDE = 8;
__global__ void matrixTransposeUnrolled(const float *_a, float *_b)
{
__shared__ float mat[TILE][TILE + 1];
int x = blockIdx.x * TILE + threadIdx.x;
int y = blockIdx.y * TILE + threadIdx.y;
#pragma unroll
for(int k = 0; k < TILE ; k += SIDE) {
if(x < rows && y + k < cols)
mat[threadIdx.y + k][threadIdx.x] = a[((y + k) * rows) + x];
}
__syncthreads();
x = blockIdx.y * TILE + threadIdx.x;
y = blockIdx.x * TILE + threadIdx.y;
#pragma unroll
for(int k = 0; k < TILE; k += SIDE) {
if(x < cols && y + k < rows)
b[(y + k) * cols + x] = mat[threadIdx.x][threadIdx.y + k];
}
}

## Slide 68: Performance for 4k x 4k Matrix Transpose (K40c)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU (Core i7 4770) | 153.6 | 0.873 |  | 
Naive Transpose | 1.078 | 124.46 | 142.48 | 142.48
Coalesced Memory | 0.998 | 134.48 | 1.080 | 153.90
Bank Conflicts | 0.994 | 134.92 | 1.004 | 154.52
Loop Unrolling | 0.772 | 173.72 | 1.287 | 198.96

## Slide 69: Transpose
Let’s review your predictions!

## Slide 70: CUDA Tips and Tricks
Don’t launch 1024 threads per block
  Prefer 256
Avoid branching
  Use templates where possible
Avoid syncthreads and global memory usage
Consider memory access patterns
Atomics on global memory is a sin
Awesome CUDA Programming Guide
Too many arguments?
  Use structures.
Use Nsight
Highly advance:
  __mul24, __umul24. Faster than * operation
  __shfl, rintf, __sin etc

## Slide 71: CIS 565 How to make the most out of it
Do all the extra credit possible, the grade really doesn't matter.
  Psst. Do extra credit after submitting (can help in final proj.)
Practice speaking about your assignments.
  It really really helps in your interview and job.
Final projects - break the bank on this one.
  This is your calling card in software programming

## Slide 72: CIS 565 How to make the most out of it
Write excellent blogs.
  Ask Patrick/3rd person to review them.
  Helps in reviewers understand your work/challenges better
Live by Git (thanks Patrick!).
  Use local repos for other classes.
  Look at Gitlab – Github like interface hosted privately
See CUDA Samples (they are really good!)
Share you knowledge
  Stackoverflow, open source contributions, forums etc.

## Slide 73: Job Advice
Do side projects, extra work - driven by motivation!
Open Source contributions = Bonus Points
Learn to write makefile
  Good practice: try converting projects to Linux
  Its really not hard
  Programs run faster on linux
  Demonstrates flexibitly to work environment
Maintain a coding style
  Doesn’t matter what style – Consistency is key
  Recommended reading: (C++) http://google-styleguide.googlecode.com/svn/trunk/cppguide.html
  Other languages: Google Style Guide

## Slide 74: Job Advice
Contribute to open source projects, take part actively in forums.
  Having an accepted contribution may mean more to development-centered companies than research.
  Forums get you noticed. Coders have high respect for people who share knowledge.
Do not settle for a job/role you do not want
  Its a burden you will not enjoy
  Don’t go after the money
Be ready to forget everything you did in school

## Slide 75: Job Advice
2 Questions to ask in every single interview:
  “How can I contribute to benefit you?”
  “How will I benefit working for you?” -> Yes, be pricey.
Only two thing matters:
  Can we enjoy working with you
  Will you enjoy working with us
Every other metric can be wrapped in those 2 points

## Slide 76: ArrayFIRE THE BEST ARE ALWAYS WELCOME HERE
We are hiring!
  Apply at: http://arrayfire.theresumator.com/apply/
  Email me: shehzan@arrayfire.com
  or visit: www.arrayfire.com
  https://github.com/arrayfire
  Twitter: @shehzanm @arrayfire

## Slide 77: Acknowledgements
NVIDIA Documentation and website
ArrayFire
UPenn CIS 565 - Patrick Cozzi

## Slide 78: Resources
CUDA Documentation: http://docs.nvidia.com/cuda/index.html
GTC On-Demand: http://on-demand-gtc.gputechconf.com/gtcnew/on-demand-gtc.php
CUDA Getting Started Windows: http://docs.nvidia.com/cuda/cuda-getting-started-guide-for-microsoft-windows/index.html
Google Style Guide C++: http://google-styleguide.googlecode.com/svn/trunk/cppguide.html
Demos and tutorials:
http://on-demand.gputechconf.com/gtc/2013/presentations/S3478-Debugging-CUDA-Kernel-Code.pdf
https://developer.nvidia.com/content/efficient-matrix-transpose-cuda-cc
http://developer.download.nvidia.com/compute/cuda/1.1-Beta/x86_website/projects/reduction/doc/reduction.pdf

## Slide 79: Reduction

## Slide 80: Reduce
Algorithm to apply a reduction operation on a set of elements to get a result.
Example:
SUM(10, 13, 9, 14) = 10+13+9+14 = 46
MAX(10, 13, 9, 14) = 14
Notes: Reduction: Any sequence of the same binary operation
Again, lets write your speedup on CPU
Hint: reduction is not as simple as transpose so don’t expect a similar speed up

## Slide 81: Serial Reduce
Loop through all elements
Number of steps: N - 1
+
+
10
13
9
+
14
46
Serial Code:
int sum = array[0];
for(i=1;i<n;i++) {
sum += array[i];
}
Number of Steps : 4-1 = 3

## Slide 82: Parallel reduce
Operations can be applied for Parallel reduce
Binary
  example: a*b, a+b, a&b, a|b
  not binary: !(a), (a)!
Associative
  example: a*b, a+b, a&b, a|b
  non associative: a/b, ab
Example:
Reduce[(10,13,9,14) +]
+
10
13
9
+
14
46
+
Number of steps: log2 4 = 2
Notes: Most parallel reductions use a binary tree structure

## Slide 83: Parallel Reduce on GPU
Parallel reduce is applied to a part of the whole array in each block.
Multiple blocks help in:
  Maximizing Occupancy by keeping SMs busy.
  Processing very large arrays.
Parallel reduce is not arithmetic intensive, it takes only 1 Flop per thread(1 add) so it is completely memory bandwidth bounded.

## Slide 84: Parallel Reduce on GPU
Need a way to communicate partial results between blocks
Global sync is not practical due to the overhead of sync across so many cores
Solution: Call the reduce kernel recursively to reduce the results from previous reduce.
Level 0:
8 Blocks
Level 1:
1 Block

## Slide 85: Serial reduce vs Parallel reduce
Serial Reduce:
  Each iteration is dependant on the previous iteration.
  Number of steps taken is n-1.
  Runtime complexity is O(n)
Parallel Reduce:
  Has smaller number steps log 2n.
  Faster than a serial implementation.
  Runtime complexity : O(log n)

## Slide 86: Method 1: Interleaved Addressing
12
14
29 | 15 | 76 | 12 | 154 | 67 | 129 | 75 | 59 | 19 | 28 | 23 | 104 | 56 | 77 | 52
14 | 15 | 64 | 12 | 87 | 67 | 54 | 75 | 40 | 19 | 5 | 23 | 48 | 56 | 25 | 52
105 | 15 | 76 | 12 | 283 | 67 | 129 | 75 | 87 | 19 | 28 | 23 | 181 | 56 | 77 | 52
388 | 15 | 76 | 12 | 154 | 67 | 129 | 75 | 268 | 19 | 28 | 23 | 104 | 56 | 77 | 52
0
2
4
6
8
10
12
0
4
8
0
8
656 | 15 | 76 | 12 | 154 | 67 | 129 | 75 | 59 | 19 | 28 | 23 | 104 | 56 | 77 | 52
0
Step 1
Step 2
Step 3
Step 4
Notes: Add 2 consecutive elements
After required steps, the element 0 will have the result

## Slide 87: Method 1: Interleaved Addressing
__global__ void reduce_stage0(int* d_idata, int* d_odata, int n) {
//Dynamic allocation of shared memory - See kernel call in host code
extern __shared__ int smem[];
//Calculate index
int idx = blockIdx.x * blockDim.x + threadIdx.x;
//Copy input data to shared memory
if(idx < n) smem[threadIdx.x] = d_idata[idx];
__syncthreads();
//Reduce within block
for(int c = 1; c < blockDim.x; c *= 2) {
if(threadIdx.x % (2*c) == 0)
smem[threadIdx.x] += smem[threadIdx.x + c];
__syncthreads();
} //Copy result of reduction to global memory
if(threadIdx.x == 0)
d_odata[blockIdx.x] = smem[0];
}
Notes: Walkthrough:
Compute index
Copy data to shared memory
Reduce interleaved in shared memory
Copy result to global

## Slide 88: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11

## Slide 89: Method 1: Interleaved Addressing
Problem?

## Slide 90: Method 1: Interleaved Addressing
Problem?
  Interleaved addressing
  Divergent warps
Solution?

## Slide 91: Method 1: Interleaved Addressing
Problem?
  Interleaved addressing
  Divergent warps
Solution?
  Non-divergent branches

## Slide 92: Warps
Divergence

## Slide 93: Warp
A thread block is broken down to 32-thread warps
Warps are executed physically in a SM(X)
Total number of warps in a block: ceil(T/Wsize)
Up to 1024
Threads
32 threads each
Up to 64 Warps/SM

## Slide 94: Warp
Each thread in a warp execute one common instruction at a time
  Warps with diverging threads execute each branch serially
if (threadIdx.x < 4) { x++; }else{ x--; }
Notes: Lets say warp size is 8
The warp is executing 3 commands instead of 2 (If statement is also a command)

## Slide 95: Warp
Each thread in a warp execute one common instruction at a time
  Warps with diverging threads execute each branch serially
if (threadIdx.x < 4) { x++; }else{ x--; }

## Slide 96: Warp
Each thread in a warp execute one common instruction at a time
  Warps with diverging threads execute each branch serially
if (threadIdx.x < 4) { x++; }else{ x--; }

## Slide 97: Warp
Each thread in a warp execute one common instruction at a time
  Warps with diverging threads execute each branch serially
if (threadIdx.x < WARP_SIZE ) { x++; }else{ x--; }

## Slide 98: Warp
Each thread in a warp execute one common instruction at a time
  Warps with diverging threads execute each branch serially
if (threadIdx.x < WARP_SIZE ) { x++; }else{ x--; }
Notes: Warp executes only 2 commands

## Slide 99: Warps - Take aways
Try to make threads per blocks to be a multiple of a warp (32)
  incomplete warps disable unused cores (waste)
  128-256 threads per blocks is a good starting point
Try to have all threads in warp execute in lock step
  divergent warps will use time to compute all paths as if they were in serial order

## Slide 100: ...back to reductions

## Slide 101: Method 2: Interleaved addressing with non divergent branch
Problem: Thread Divergence
if (tid % (2*s) == 0) sdata[tid] += sdata[tid+s];
Solution: Replace with non divergent branch
  uses half the number of threads as before
int index = 2 * s * tid;
if (index < blockDim.x) {
sdata[index] += sdata[index + s]; } __syncthreads();
s=2
tid = 0
tid=256
tid=3
tid=53
thread 3 and 53 are idle
Notes: Previous version:
for(int c = 1; c < blockDim.x; c *= 2) { if(threadIdx.x % (2*c) == 0) smem[threadIdx.x] += smem[threadIdx.x + c]; __syncthreads(); }
New Version:
for(int c = 1; c < blockDim.x; c *= 2) { int index = 2 * c * threadIdx.x; if(index < blockDim.x) smem[index] += smem[index + c]; __syncthreads(); }

## Slide 102: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11
Stage 1 | 6.26 | 21.45 | 1.26 | 1.41

## Slide 103: Method 2
Problem:
Bank conflict
  Each thread accesses adjacent memory locations resulting in shared memory bank conflict.
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Solution:
  Resolve bank conflicts.
t0 | t1 | t2 | t3 | t4 | t5
Bank
Threads in a Warp

## Slide 104: Method 3: Removing Bank Conflicts
14 | 15 | 64 | 12 | 87 | 67 | 54 | 75 | 40 | 19 | 5 | 23 | 48 | 56 | 25 | 52
54 | 34 | 69 | 35 | 135 | 123 | 79 | 127 | 59 | 19 | 28 | 23 | 104 | 56 | 77 | 52
656 | 319 | 148 | 162 | 135 | 123 | 79 | 127 | 59 | 19 | 28 | 23 | 104 | 56 | 77 | 52
Step 1
Final Step 4
0
1
2
3
4
5
6
7
Notes: Instead of adding adjacent elements, add elements in adjacent blocks

## Slide 105: Method 3 : Sequential reduction
for(unsigned int s=blockDim.x/2; s>0; s>>=1) {
if (tid < s) { sdata[tid] += sdata[tid + s];
}
__syncthreads();
}
for(unsigned int s=1; s < blockDim.x; s *= 2) {
int index = 2 * s * tid;
if (index < blockDim.x) { sdata[index] += sdata[index + s]; } __syncthreads();
}
Replace the interleaved addressing in for loop of Method 2
With reversed loop thread id based indexing in Method 3
Notes: S>>=1 is s = s / 2

## Slide 106: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11
Stage 1 | 6.26 | 21.45 | 1.26 | 1.41
Stage 2 | 4.70 | 28.54 | 1.33 | 1.87

## Slide 107: Method 3: Sequential Reduction
Problem:
  In the first iteration itself half of the threads in each block are wasted, only half of them perform the reduction
Solution:
  Reduce the number of threads to half in each block.
  Make each thread read 2 elements to the shared memory.
Perform first reduction during first read.
Notes: Half the warps are not doing anything because of the adding increment condition S >> =1

## Slide 108: Method 4: Add on Load (Multiple Elements/Thread)
// reading from global memory, writing to shared memory
unsigned int tid = threadIdx.x;
unsigned int i = blockIdx.x * blockDim.x * 2 + threadIdx.x; sdata[tid] = g_idata[i] + g_idata[i+blockDim.x];
__syncthreads();
// each thread loads one element from global to shared mem unsigned int tid = threadIdx.x; unsigned int i = blockIdx.x*blockDim.x + threadIdx.x; sdata[tid] = g_idata[i];
__syncthreads();
Until now each thread loaded one element to the shared memory.
Half the number of threads. Make each thread read in two values from global memory, perform reduction and write result to shared memory

## Slide 109: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11
Stage 1 | 6.26 | 21.45 | 1.26 | 1.41
Stage 2 | 4.70 | 28.54 | 1.33 | 1.87
Stage 3 (2 elements / thread) | 2.84 | 47.22 | 1.65 | 3.10

## Slide 110: Method X : Multiple adds / thread
Replace single add with a loop.
Use a counter TILE to define the number to adds per thread
  defining TILE as global constant will allow loop unrolling
  preferable set TILE as power of 2
Notes: Substitute 2 adds per load by TILE adds per load.
Similar to loops in transpose

## Slide 111: Method X : Multiple adds / thread
//in global space
const int TILE = 4;
//in kernel
extern __shared__ int smem[];
int idx = blockIdx.x * blockDim.x * TILE + threadIdx.x;
int tid = threadIdx.x;
if(idx < n) {
smem[tid] = 0;
for(int c = 0; c < TILE; c++) { //can use #pragma unroll here
if(idx + c * blockDim.x < n)
smem[tid] += d_idata[idx + c * blockDim.x];
}
}
__syncthreads();

## Slide 112: Method 5 : Last Warp Unroll
Write a device function “warpReduce” to be called by all threads with threadIdx.x < 32
__device__ void warpReduce(volatile int* sdata, int tid) {
sdata[tid] += sdata[tid + 32];
sdata[tid] += sdata[tid + 16];
sdata[tid] += sdata[tid + 8];
sdata[tid] += sdata[tid + 4];
sdata[tid] += sdata[tid + 2];
sdata[tid] += sdata[tid + 1];
}
Observe that volatile is used to declare sdata, so that the compiler doesn't reorder stores to it and induce incorrect behavior.
Notes: Explicitly unroll last warp
Allows compiler to make more optimizations

## Slide 113: Method 5 : Last Warp Unroll
Rewrite inner loop as:
for (unsigned int s=blockDim.x/2; s>32; s>>=1) {
if (tid < s) sdata[tid] += sdata[tid + s];
__syncthreads();
}
if (tid < 32) warpReduce(sdata, tid);

## Slide 114: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11
Stage 1 | 6.26 | 21.45 | 1.26 | 1.41
Stage 2 | 4.70 | 28.54 | 1.33 | 1.87
Stage 3 (2 elements / thread) | 2.84 | 47.22 | 1.65 | 3.10
Stage 4 (32 elements / thread) | 0.91 | 147.89 | 3.13 | 9.70

## Slide 115: Method 6 : Complete Unroll
Problem:
  Now we come down to inner for loop lowering the performance.
Solution:
  Unroll the for loop entirely.
  Possible only if the block size is known beforehand.
  Block size in GPU limited to 512 or 1024 threads.
  Also make block sizes power of 2 (preferably multiples of 32).

## Slide 116: Method 6 : Complete Unroll
But block sizes is not known at compile time.
Solution :
  Use Templates
  CUDA supports C++ template parameters on device and host functions
  Specify block size as a function template parameter:
template <unsigned int blockSize>
__global__ void reduce4(int *g_idata, int *g_odata)

## Slide 117: Method 6 : Complete Unroll
Loop Unroll:
  if (blockSize >= 1024) { if (tid < 512) { sdata[tid] += sdata[tid + 512]; } __syncthreads(); }
  if (blockSize >= 512) {
  if (tid < 256) { sdata[tid] += sdata[tid + 256]; } __syncthreads(); }
  if (blockSize >= 256) {
  if (tid < 128) { sdata[tid] += sdata[tid + 128]; } __syncthreads(); }
  if (blockSize >= 128) { if (tid < 64) { sdata[tid] += sdata[tid + 64]; } __syncthreads(); }
  if (tid< 32) warpReduce<blockSize>(sdata, tid.x);
The block size is known at compile time, so all the code in red is evaluated at compile time.
In the main host code add :
// number of threads in the block = 256
reduce<256><<< dimGrid, dimBlock, smemSize >>>(d_idata, d_odata);

## Slide 118: Method 6 : Complete Unroll
Also template the device warpReduce function
//Using templates, blockSize will be defined at compile time
template <unsigned int blockSize>
__device__ void warpReduce(volatile int* sdata, int tid) {
sdata[tid] += sdata[tid + 32];
sdata[tid] += sdata[tid + 16];
sdata[tid] += sdata[tid + 8];
sdata[tid] += sdata[tid + 4];
sdata[tid] += sdata[tid + 2];
sdata[tid] += sdata[tid + 1];
}

## Slide 119: Performance for 32M elements (GTX 770)
 | Time (ms) | Bandwidth (GB/s) | Step Speedup | Speed Up vs CPU
CPU (Intel Core i7 4770K) | 8.8 | 15.25 |  | 
Stage 0 | 7.90 | 16.98 | 1.11 | 1.11
Stage 1 | 6.26 | 21.45 | 1.26 | 1.41
Stage 2 | 4.70 | 28.54 | 1.33 | 1.87
Stage 3 (2 elements / thread) | 2.84 | 47.22 | 1.65 | 3.10
Stage 4 (32 elements / thread) | 0.91 | 147.89 | 3.13 | 9.70
Stage 5 (32 elements / thread) | 0.87 | 154.18 | 1.04 | 10.11

## Slide 120: Performance Comparison

## Slide 121: Overview of Basics
kernel: C/C++ function which executes on the device
thread: lightweight thread that runs on the device
block: collection of threads
grid: collection of all blocks launched
Notes: Rubix cube

## Slide 122: Parallel Execution
Blocks are a group of threads
  Each block has a unique ID which is accessed by the blockIdx variable
  Threads in the same block share a very fast local memory called shared memory
  Organized in a 1D, 2D, or 3D grid
  You can have a maximum of 2048M x 64K x 64K grid of blocks
  Each block executes on an SM in unspecified order
Notes: Built in variables
Use CUDA device query (look in samples) or GPU caps viewer so see your specs

## Slide 123: Grid: 1D/2D/3D Collection of Blocks
blockIdx.x
blockIdx.y
blockIdx.z
(3, 2, 0)
x y z
Notes: Think in terms of dimensions rather than row and column

## Slide 124: Block: 1D/2D/3D Collection of Threads
CUDA
threads
arranged
in a
32 x 4 x 1 pattern inside each Block
Notes: This is a sample arrangement.
A block could have 1024 linear threads or 32x32 2D threads or any other acceptable form of arrangement

## Slide 125: Basic Control Flow
1. Allocate memory on the device
2. Copy data from host memory to device memory
3. Launch: kernel<<<..>>>
4. Retrieve results from GPU memory to CPU memory

## Slide 126: Parallel Execution
Execution Path
The same CUDA program gets its thread blocks distributed automatically across any given SM architecture.

## Slide 127: Memory Hierarchy
global, local, shared

## Slide 128: Memory Hierarchy

## Slide 129: Memory Hierarchy
Global Memory
  Created using cudaMalloc
  Available to all threads
__global__ void add(int* a, int* b, int* c) { int id = blockIdx.x*blockDim.x
+ threadIdx.x;
c[id] = a[id] + b[id]; }

## Slide 130: Memory Hierarchy
Local Memory
  Stored in registers (very fast)
  Thread local
__global__ void add(int* a, int* b, int* c) { int id = blockIdx.x*blockDim.x
+ threadIdx.x;
c[id] = a[id] + b[id]; }

## Slide 131: Memory Hierarchy
__global__ void add(int* a, int* b, int* c) { __shared__ int aValues[BLOCK_SIZE];
__shared__ int bValues[BLOCK_SIZE];
int id = threadIdx.x;
int globalId = blockIdx.x * BLOCK_SIZE + threadIdx.x;
aValues[id] = a[globalId];
bValues[id] = b[globalId]; c[id] = aValues[id] + bValues[id]; }
Shared Memory
  Located on the GPU's SM
  User managed
  Fast (like registers)
  Accessible by all threads in the block

## Slide 132: Running CUDA-GDB (Linux)
Debugging requires pausing the GPU
  If the desktop manager is running on the GPU then it will become unusable.
Single GPU debugging
  Stop the desktop manager
    On Linux: sudo service gdm stop
    On Mac OS X you can log in with the >console user name
Multi-GPU debugging
  In Linux the driver excludes GPUs used by X11
  On Mac OS X you can set which device to expose to cuda-gdb by setting the CUDA_VISIBLE_DEVICES environment variable
Notes: cuda-gdb requires 2 gpus to debug. X11 system does not allow gpu debugging access.
Alternatives are to use ssh or use CLI mode with no X system