## Slide 1: Realistically Bad Data
Liam Boone
September 29th, 2014

## Slide 2: About Me
Pennsylvania State University (2007 – 2012)
  B.S. in Electrical Engineering
  B.S. in Computer Engineering
University of Pennsylvania (2012 – 2014)
  M.S.E. in Computer & Information Science
Sandia National Labs (2012 – Now)

## Slide 3: My History with CIS 565
Chart: 
| 2012 - Student | 2013 - TA | 2014 - Guest
Power | 1 | 2 | 4
Responsibility | 1 | 3 | 0.1

## Slide 4: Globe Rendering
All world and cloud textures courtesy of NASA’s MODIS datasets

## Slide 5: Motivation
Strong need for payload agnostic simulation of real-time data
Introduce more dynamic scene elements to allow greater flexibility for algorithm developers
  Current test data has static backgrounds and little to no bad pixels
  Would allow developers to test on realistic scenes
Goals:
  Faster development cycles and fewer bugs in software
  Dynamically produce realistic scenes to provide developers with a larger library of test scenarios

## Slide 6: Processing Flow
Generate Rays for Each Pixel
Intersect Rays with Earth Model
Calculate Intensities

## Slide 7: Generate Rays
Rays form a one-to-one correspondence with Pixels in the simulated focal plane
  Each Ray originates at the center of an idealized camera located at some position in space and extends through an imaginary focal plane located some distance in front of the idealized camera
  For this we need to know:
    Position of the camera
    Rotation of the camera (to determine where it is looking)
    Resolution of the focal plane (number of pixels wide/tall)
    Field of view of the camera
Focal Point
Focal plane
Rays
Field of View
Earth

## Slide 8: Sensor Jitter
The camera is not perfect and will move from frame to frame
Represented as a rotation from true pointing direction
  Euler angles (Roll, Pitch, Yaw)
  Very small
  Random values sampled from N-D Gaussian distribution
  Over time the look angle will walk off from where it should be
Roll
Yaw
Pitch

## Slide 9: Ray Intersection
All models use simple spheres as primitives
  Straight-forward intersection routine
  Use formula for sphere () and ray () to derive an intersection point
  Boils down to a familiar quadratic equation ()
Helps with computational complexity
  Code reuse
  Easy to manage

## Slide 10: Earth Model (Simple)
Simple Earth Model
  Two concentric spheres
  Inner sphere represents the surface of the earth
  Outer sphere is the cloud layer
Details are represented by textures
  No height data involved
  Intensity values from NASA MODIS
  Clouds are “flattened” into one layer
Pros
  Easy to code
  Fast
Earth
Clouds
Cons
  Not very realistic
  Some test cases hard to represent

## Slide 11: Earth Model (Complex)
Earth
Clouds
Complex Earth Model
  Three concentric spheres
  Inner two spheres as before
  Outer sphere is the extent of the atmosphere
Atmosphere layer contributes scattering
  Rayleigh and Mie scattering
  Must evaluate a double integral per pixel
  Wavelength dependent
Pros
  More accuracy
  More test cases
Atmosphere
Cons
  Still not perfect
  Requires much more computation

## Slide 12: Intensity calculation
Terrain Reflectance
Cloud Obscuration
Atmospheric Attenuation
Noise

## Slide 13: Terrain
From the ray/sphere intersection point determine a Lat/Lon coordinate
Sample from an image representing the surface of the earth to get the base intensity
Sample from a binary image representing whether a given coordinate is water or not to get the specular coefficient
Use simple Phong lighting model to apply diffuse and specular components of the sun’s light

## Slide 14: Clouds
From the ray/sphere intersection point determine a lookup coordinate
Sample the cloud image to determine a cloud density value
Use the density value to attenuate the intensity of the ground
Can also use a second ray cast to the sun to determine if the clouds will cast a shadow on the surface of the earth

## Slide 15: Atmosphere I
Attenuation based on distance light travels through the atmosphere
Calculated with a double integral
Attenuation Factor:
Phase Function:
Out-Scattering Function:
In-Scattering Function:

## Slide 16: Atmosphere II
: Molecular density at sea level
: Wavelength of detectable light
: Angle between incident light and viewing vector
: Scattering parameter
  0 for Rayleigh
  Between -0.75 and -0.999 for Mie
: Scale height of the atmosphere
: Height above surface of the earth
: Points (see figure on next slide)

## Slide 17: Atmosphere III

## Slide 18: Scattering Results
All world and cloud textures courtesy of NASA’s MODIS datasets

## Slide 19: Intensity Calculation (Noise)
Shot noise
  Simulates a more grainy image
  Use a Poisson distribution centered on the pixel value
  Variable with time
Popcorn noise
  Simulates under/over-excited pixels
  Sample a uniform distribution and saturate or zero the pixel if the sample is above or below some threshold respectively
  Variable with time
Fixed pattern noise
  Simplest noise type
  Defines a fixed pattern of dead/under-excitable pixels
  Constant over the lifetime of the simulation

## Slide 20: Shot Noise
Knuth’s Poisson sampling algorithm:
Can be parameterized by multiplying λ by some constant s before sampling and then dividing by the same constant afterwards
  Small values of s lead to more grainy images
  Large values of s cause the algorithm to perform slower
Def Poisson(λ):
Let L ← exp(−λ), k ← 0 and p ← 1.
do:
k ← k + 1.
Generate uniform random number u in [0,1].
let p ← p × u.
while p > L.
return k − 1.
Poisson(λ*s)/s

## Slide 21: Shot Noise
Test Pattern
Noise (s=2)

## Slide 22: Shot Noise
Test Pattern
Noise (s=1)

## Slide 23: Shot Noise
Test Pattern
Noise (s=0.1)

## Slide 24: Popcorn Noise
Popcorn sampling algorithm:
Def Popcorn(x, t):
Generate uniform random number u in [0,1].
If u > (1-t):
return 255.
If u < t:
return 0.
return x.

## Slide 25: Popcorn Noise
Test Pattern
Noise (t=0.001)

## Slide 26: Popcorn Noise
Test Pattern
Noise (t=0.1)

## Slide 27: Fixed Pattern Noise
Fixed pattern noise is simply a constant offset or attenuation applied to the whole FPA
Simulates manufacturing defects and errors present in the hardware

## Slide 28: Fixed Pattern Noise
Test Pattern
Noise (Horizontal Bars)

## Slide 29: All Together
Test Pattern
Noise (p=0.1, t = 0.01, Bars)

## Slide 30: Terrain Rendering

## Slide 31: Overview
Atmospherics and sensor noise are great first steps
Good enough for some situations
Sometimes necessary to fully model the terrain
  Need terrain data to answer questions about where mountain shadows lie
  Is a particular asset’s view obstructed by terrain in any way?
Current dataset chosen is DTED level 1
  Partial global coverage
  90m post spacing in most of the world

## Slide 32: Algorithm
Preprocess data into a chunked maximum mipmap format
  Each entry in each level of the mipmap represents the maximum height of the four entries in the next finer level
  A 513x513 chunk of elevation posts give a 512x512 initial level
  Generate coarser levels until one value is reached
  Chunk edges will share posts
Ray march through the mipmap structure
  Step through progressively finer levels of the mipmap until the finest layer is encountered or the ray steps off of the chunk
Intersect the ray with a bilinear patch to determine the final elevation of the terrain

## Slide 33: Maximum Mipmap (2D)

## Slide 34: Maximum Mipmap (2D)

## Slide 35: Maximum Mipmap (2D)

## Slide 36: Maximum Mipmap (2D)

## Slide 37: Maximum Mipmap (2D)

## Slide 38: Maximum Mipmap (2D)

## Slide 39: Maximum Mipmap (2D)

## Slide 40: Maximum Mipmap (2D)

## Slide 41: Maximum Mipmap (2D)

## Slide 42: Bilinear Patch Intersection
Intersect a ray with a bilinear surface
Substitute ray equation into patch equation
Solve for t
  Solve like sphere intersection
  Make sure to stay inside of patch bounds
  Ray can have 0, 1, or 2 intersection points

## Slide 43: Results – Maximum Mipmap
Green channel used to indicate number of steps before surface intersection
Blue channel indicates height of terrain

## Slide 44: Results – Bilinear Patch Intersection
Color represents intersection position
Shading based on patch normals

## Slide 45: Questions?

## Slide 46: References
Schafhitzel, Tobias, Martin Falk, and Thomas Ertl. "Real-time rendering of planets with atmospheres." (2007).
O’Neil, Sean. "Accurate atmospheric scattering." GPU Gems 2 (2005): 253-268.
Dick, Christian, Jens Krüger, and Rüdiger Westermann. "GPU ray-casting for scalable terrain rendering." Proceedings of EUROGRAPHICS. Vol. 50. 2009.
Tevs, Art, Ivo Ihrke, and Hans-Peter Seidel. "Maximum mipmaps for fast, accurate, and scalable dynamic height field rendering." Proceedings of the 2008 symposium on Interactive 3D graphics and games. ACM, 2008.
http://modis.gsfc.nasa.gov/ - MODIS Texture Data